## Slide 1: Multi-sensor rail track detection in automatic train operations
Master’s thesis in Data Science
Student: Attila Kovacs
1st Advisor: Lukas Rohatsch (UAS Technikum Wien)
2nd Advisor: Daniele Capriotti (M2C Expert Control GmbH)
Alignment: 30.04.2024
Confidential - Do not share

## Slide 2: Outline
Motivation
Datasets
Solution approach
  Traditional approach – Fast line detection
  Deep learning approach – YOLOv8
Results
Conclusion

## Slide 3: Motivation
Automatic train operations (ATO)
ATO systems use advanced technologies to perceive and interpret the railway environment to facilitate autonomous operations with minimal human intervention
Automatic rail track detection
Computer vision-based rail track detection is a crucial component for autonomous train navigation as it enables trains to understand and navigate complex rail networks with minimal human intervention

## Slide 4: Motivation
Input: images generated by different sensors mounted on locomotive
Goal: identify and segment rail tracks

## Slide 5: Dataset
OSDaR23 dataset (Digitale Schiene / Deutsche Bahn)  Training and evaluation
  7.421 frames from 45 video sequences
  27.386 labels
  Low/high resolution RGB camera and infrared camera
RailSem19 dataset (Austrian Institute of Technology)  Training
  8.500 images
  58.483 labels
  Only RGB images
Video stream (M2C / DB Cargo)  Evaluation
  1:14h video
  Different scenarios such as tunel, double/single track, side walls etc.

## Slide 6: Solution approach
Non-AI-based segmentation with fast line detection
  Detect edges in image
  Extract line segments
  Grouping of line segments based on orientation and proximity
Deep-learning based approach based on YOLOv8
  Train model with pre-labeled images
  Classify each pixel in an image according to its category (rail tracks vs. background)
  Convert pixels into polylines
Evaluation criterion
  Dice score – best suited for unbalanced datasets, e.g., when the background is dominant

## Slide 7: Non-AI-based segmentation with fast line detection (FLD)
Labels are given in the dataset
Filtering by removing „unusual“ lines
Apply FLD
Removing noise based on clustering

## Slide 8: Deep-learning based approach based on YOLOv8
There are differenet applications in AI-based computer vision

## Slide 9: Deep-learning based approach based on YOLOv8
In each step of the training process, the model is provided with labeled images
The model is evaluated on images from the validation set

## Slide 10: Results – Visual inspection
Ground truth
FLD
YOLO

## Slide 11: Results – FLD vs. YOLOv8 on OSDaR23

## Slide 12: Results – Video stream: incorportating domain knowledge

## Slide 13: Conclusion
First project to investigate different sensor types in rail track detection
Devised traditional base-line approach (FLD) and AI-based approach (YOLO)
YOLO outperforms FLD in almost all test images based on Dice-score
YOLO seems to provide very good results on infrared images
Best performace is achieved if AI-based track detection is enhanced by domain knowledge

## Slide 14: Thank you for the data/video and the attention!