## Slide 1: Multi-sensor rail track detection in automatic train operations
Master’s thesis in Data Science
Student: Attila Kovacs
1st Advisor: Lukas Rohatsch (UAS Technikum Wien)
2nd Advisor: Daniele Capriotti (M2C Expert Control GmbH)
26.06.2024

## Slide 2: Motivation
Automatic train operations (ATO)
ATO systems use advanced technologies to interpret the railway environment to facilitate autonomous operations with minimal human intervention
Automatic rail track detection
Computer vision-based rail track detection is a crucial component that enables autonomous train navigation in complex rail networks

## Slide 3: Motivation
Input: images generated by different sensors mounted on locomotive
Goal: identify and segment rail tracks

## Slide 4: Dataset
OSDaR23 dataset (Digitale Schiene / Deutsche Bahn)  Training and evaluation
  7.421 frames from 45 video sequences
  27.386 labels
  Low/high resolution RGB camera and infrared camera
RailSem19 dataset (Austrian Institute of Technology)  Training
  8.500 images
  58.483 labels
  Only RGB images
Video stream (M2C / DB Cargo)  Evaluation
  1:14h video
  Different scenarios such as tunel, double/single track, side walls etc.

## Slide 5: Solution approach
Non-AI-based segmentation with fast line detection (FLD)
  Detect edges in image
  Extract line segments
  Grouping of line segments based on orientation and proximity
Deep-learning based approach based on YOLOv8
  Train model with pre-labeled images
  Classify each pixel in an image according to its category (rail tracks vs. background)
  Convert pixels into polylines
Evaluation criterion
  Dice score – best suited for unbalanced datasets, e.g., when the background is dominant

## Slide 6: Results – Visual inspection
Ground truth
FLD
YOLO

## Slide 7: Results – FLD vs. YOLOv8 on OSDaR23
Each point denotes one image

## Slide 8: Results – Video stream: incorportating domain knowledge

## Slide 9: Conclusion
First project to investigate different sensor types in rail track detection
Devised traditional base-line approach (FLD) and AI-based approach (YOLO)
YOLO outperforms FLD in almost all test images based on Dice-score
YOLO seems to provide very good results on infrared images
Best performace is achieved if AI-based track detection is enhanced by domain knowledge

## Slide 10: Thanks!

## Slide 11: Automatic train operations

## Slide 12: Challenges
Size of dataset becomes often a limiting factor (disk, RAM, CPU)
Refactoring existing approaches for lane detection proved difficult
Organization of experiments
A lot of custom code
Resource intensive training despite HPC
Working with HPC (scheduling, data transfer, versioning)
Model tuning can take up to one week

## Slide 13: Non-AI-based segmentation with fast line detection (FLD)
Labels are given in the dataset
Filtering by removing „unusual“ lines
Apply FLD
Removing noise based on clustering

## Slide 14: Deep-learning based approach based on YOLOv8
There are differenet applications in AI-based computer vision

## Slide 15: Deep-learning based approach based on YOLOv8
In each step of the training process, the model is provided with labeled images
The model is evaluated on images from the validation set

## Slide 16: Results per sensor

## Slide 17: Labelling approaches

## Slide 18: Tested YOLOv8 models

## Slide 19: Frames of a video sequence

## Slide 20: Performance metrics